## Table A-II/2

#### Specification of minimum standard of competence for masters and chief mates

#### on ships of 500 gross tonnage or more

# Function: Navigation at the management level

| Column 1 | Column 2 | Column 3 | Column 4 |
| --- | --- | --- | --- |
| COMPETENCE | KNOWLEDGE, UNDERSTANDING AND PROFICIENCY | METHODS FOR DEMONSTRATING COMPETENCE | CRITERIA FOR EVALUATING COMPETENCE |
| Plan a voyage and conduct navigation | Voyage planning and navigation for all conditions by acceptable methods of plotting ocean tracks, taking into account, e.g.: .1 restricted waters .2 meteorological conditions .3 ice .4 restricted visibility .5 traffic separation schemes .6 areas of extensive tidal effects Routeing in accordance with the General Principles on Ships' Routeing Reporting in accordance with the Guidelines and Criteria for Ship Reporting Systems | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved laboratory equipment training using: chart catalogues, charts, nautical publications and ship particulars | The equipment, charts and nautical publications required for the voyage are enumerated and appropriate to the safe conduct of the voyage. The reasons for the planned route are supported by facts and statistical data obtained from relevant sources and publications. Positions, courses, distances and time calculations are correct within accepted accuracy standards for navigational equipment. All potential navigational hazards are accurately identified. |
| Determine position and the accuracy of resultant position fix by any means | Position determination in all conditions: .1 by celestial observations .2 by terrestrial observations, including the ability to use appropriate charts, notices to mariners and other publications to assess the accuracy of the resulting position fix .3 using modern electronic navigational aids, with specific knowledge of their operating principles, limitations, sources of error, detection of misrepresentation of information and methods of correction to obtain accurate position fixing | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved laboratory equipment training using: .1 charts, nautical almanac, plotting sheets, chronometer, sextant and a calculator .2 charts, navigational publications and instruments (azimuth mirror, sextant, log, sounding equipment, compass) and manufacturers' manuals .3 radar, Decca, Loran, satellite navigation systems and appropriate navigational charts and publications | The primary method chosen for fixing the ship's position is the most appropriate to the prevailing circumstances and conditions The fix obtained by celestial observations is within accepted accuracy levels The fix obtained by terrestrial observations is within accepted accuracy levels The accuracy of the resulting fix is properly assessed The fix obtained by the use of electronic navigational aids is within the accuracy standards of the systems in use. The possible errors affecting the accuracy of the resulting position are stated and methods of minimizing the effects of system errors on the resulting position are properly applied |
| Determine and allow for compass errors | Ability to determine and allow for errors of the magnetic and gyro-compasses Knowledge of the principles of magnetic and gyro-compasses An understanding of systems under the control of the master gyro and a knowledge of the operation and care of the main types of gyro-compass | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved laboratory equipment training using: celestial observations, terrestrial bearings and comparison between magnetic and gyro-compasses | The method and frequency of checks for errors of magnetic and gyro-compasses ensures accuracy of information |
| Co-ordinate search and rescue operations | A thorough knowledge of and ability to apply the procedures contained in the IMO Merchant Ship Search and Rescue Manual (MERSAR) | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved laboratory equipment training using: relevant publications, charts, meteorological data, particulars of ships involved, radiocommunication equipment and other available facilities and one or more of the following: .1 approved SAR training course .2 approved simulator training, where appropriate .3 approved laboratory equipment training | The plan for co-ordinating search and rescue operations is in accordance with international guidelines and standards Radiocommunications are established and correct communication procedures are followed at all stages of the search and rescue operations |
| Establish watchkeeping arrangements and procedure | Thorough knowledge of content, application and intent of the International Regulations for Preventing Collisions at Sea Thorough knowledge of the content, application and intent of the Principles to be observed in keeping a navigational watch. Effective bridge teamwork procedures | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate | Watchkeeping arrangements and procedures are established and maintained in compliance with international regulations and guidelines so as to ensure the safety of navigation, protection of the marine environment and safety of the ship and persons on board. |
| Maintain safe navigation through the use of radar and ARPA and modern navigation systems to assist command decision-making Note: Training and assessment in the use of ARPA is not required for those who serve exclusively on ships not fitted with ARPA. This limitation shall be reflected in the endorsement issued to the seafarer concerned. | An appreciation of system errors and thorough understanding of the operational aspects of modern navigational systems, including radar and ARPA Blind pilotage techniques Evaluation of navigational information derived from all sources, including radar and ARPA, in order to make and implement command decisions for collision avoidance and for directing the safe navigation of the ship The inter-relationship and optimum use of all navigational data available for conducting navigation | Assessment of evidence obtained from approved radar simulator and ARPA simulator training | Information obtained from radar and ARPA is correctly interpreted and analysed, taking into account the limitations of the equipment and prevailing circumstances and conditions Action taken to avoid a close encounter or collision with another vessel is in accordance with the International Regulations for Preventing Collisions at Sea |
| Forecast weather and oceanographic conditions | Ability to understand and interpret a synoptic chart and to forecast area weather, taking into account local weather conditions and information received by weather fax Knowledge of the characteristics of various weather systems, including tropical revolving storms and avoidance of storm centres and the dangerous quadrants Knowledge of ocean current systems Ability to calculate tidal conditions Use all appropriate navigational publications on tides and currents | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved laboratory equipment training | The likely weather conditions predicted for a determined period are based on all available information Actions taken to maintain safety of navigation minimize any risk to safety of the ship Reasons for intended action are backed by statistical data and observations of the actual weather conditions |
| Respond to navigational emergencies | Precautions when beaching a ship Action to be taken if grounding is imminent, and after grounding Refloating a grounded ship with and without assistance Action to be taken if collision is imminent and following a collision or impairment of the watertight integrity of the hull by any cause Assessment of damage control Emergency steering Emergency towing arrangements and towing procedure | Examination and assessment of evidence obtained from practical instruction, in-service experience and practical drills in emergency procedures | The type and scale of any problem is promptly identified and decisions and actions minimize the effects of any malfunction of the ship's systems Communications are effective and comply with established procedures Decisions and actions maximize safety of persons on board |
| Manoeuvre and handle a ship in all conditions | Manoeuvring and handling a ship in all conditions, including: .1 manoeuvres when approaching pilot stations and embarking or disembarking pilots, with due regard to weather, tide, headreach and stopping distances .2 handling ship in rivers, estuaries and restricted waters, having regard to the effects of current, wind and restricted water on helm response .3 application of constant rate of turn techniques .4 manoeuvring in shallow water, including the reduction in under-keel clearance caused by squat, rolling and pitching .5 interaction between passing ships and between own ship and nearby banks (canal effect) .6 berthing and unberthing under various conditions of wind, tide and current with and without tugs .7 ship and tug interaction .8 use of propulsion and manoeuvring systems .9 choice of anchorage; anchoring with one or two anchors in limited anchorages and factors involved in determining the length of anchor cable to be used .10 dragging anchor; clearing fouled anchors .11 dry-docking, both with and without damage .12 management and handling of ships in heavy weather, including assisting a ship or aircraft in distress; towing operations; means of keeping an unmanageable ship out of trough of the sea, lessening drift and use of oil .13 precautions in manoeuvring to launch rescue boats or survival craft in bad weather .14 methods of taking on board survivors from rescue boats and survival craft .15 ability to determine the manoeuvring and propulsion characteristics of common types of ships with special reference to stopping distances and turning circles at various draughts and speeds .16 importance of navigating at reduced speed to avoid damage caused by own ship's bow wave and stern wave .17 practical measures to be taken when navigating in or near ice or in conditions of ice accumulation on board .18 use of, and manoeuvring in and near, traffic separation schemes and in vessel traffic service (VTS) areas | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved manned scale ship model, where appropriate | All decisions concerning berthing and anchoring are based on a proper assessment of the ship's manoeuvring and engine characteristics and the forces to be expected while berthed alongside or lying at anchor While under way, a full assessment is made of possible effects of shallow and restricted waters, ice, banks, tidal conditions, passing ships and own ship's bow and stern wave so that the ship can be safely manoeuvred under various conditions of loading and weather |
| Operate remote controls of propulsion plant and engineering systems and services | Operating principles of marine power plants Ships' auxiliary machinery General knowledge of marine engineering terms | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate | Plant, auxiliary machinery and equipment is operated in accordance with technical specifications and within safe operating limits at all times |

# Function: Cargo handling and stowage at the management level

| Column 1 | Column 2 | Column 3 | Column 4 |
| --- | --- | --- | --- |
| COMPETENCE | KNOWLEDGE, UNDERSTANDING AND PROFICIENCY | METHODS FOR DEMONSTRATING COMPETENCE | CRITERIA FOR EVALUATING COMPETENCE |
| Plan and ensure safe loading, stowage, securing, care during the voyage and unloading of cargoes | Knowledge of and ability to apply relevant international regulations, codes and standards concerning the safe handling, stowage, securing and transport of cargoes Knowledge of the effect on trim and stability of cargoes and cargo operations Use of stability and trim diagrams and stress-calculating equipment, including automatic data-based (ADB) equipment, and knowledge of loading cargoes and ballasting in order to keep hull stress within acceptable limits Stowage and securing of cargoes on board ships, including cargo-handling gear and securing and lashing equipment Loading and unloading operations, with special regard to the transport of cargoes identified in the Code of Safe Practice for Cargo Stowage and Securing General knowledge of tankers and tanker operations Knowledge of the operational and design limitations of bulk carriers Ability to use all available shipboard data related to loading, care and unloading of bulk cargoes Ability to establish procedures for safe cargo handling in accordance with the provisions of the relevant instruments such as BC Code, IMDG Code, MARPOL 73/78, Annexes III and V and other relevant information Ability to explain the basic principles for establishing effective communications and improving working relationship between ship and terminal personnel | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate using: stability, trim and stress tables, diagrams and stress-calculating equipment. | The frequency and extent of cargo condition monitoring is appropriate to its nature and prevailing conditions Unacceptable or unforeseen variations in the condition or specification of the cargo is promptly recognized and remedial action is immediately taken and designed to safeguard the safety of the ship and those on board Cargo operations are planned and executed in accordance with established procedures and legislative requirements Stowage and securing of cargoes ensures that stability and stress conditions remain within safe limits at all times during the voyage |
| Assess reported defects and damages to cargo spaces, hatch covers and ballast tanks and take appropriate action | Knowledge of the limitations on strength of the vital constructional parts of a standard bulk carrier and ability to interpret given figures for bending moments and shear forces Ability to explain how to avoid the detrimental effects on bulk carriers of corrosion, fatigue and inadequate cargo handling | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate using: stability, trim and stress tables, diagrams and stress-calculating equipment | Evaluations are based on accepted principles, well-founded arguments and correctly carried out. The decisions taken are acceptable, taking into consideration the safety of the ship and the prevailing conditions |
| Carriage of dangerous goods | International regulations, standards, codes and recommendations on the carriage of dangerous cargoes, including the International Maritime Dangerous Goods (IMDG) Code and the Code of Safe Practice for Solid Bulk Cargoes (BC Code). Carriage of dangerous, hazardous and harmful cargoes; precautions during loading and unloading and care during the voyage | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved simulator training, where appropriate .3 approved specialist training | Planned distribution of cargo is based on reliable information and is in accordance with established guidelines and legislative requirements Information on dangers, hazards and special requirements is recorded in a format suitable for easy reference in the event of an incident |

# Function: Controlling the operation of the ship and care for persons on board at the management level

| Column 1 | Column 2 | Column 3 | Column 4 |
| --- | --- | --- | --- |
| COMPETENCE | KNOWLEDGE, UNDERSTANDING AND PROFICIENCY | METHODS FOR DEMONSTRATING COMPETENCE | CRITERIA FOR EVALUATING COMPETENCE |
| Control trim, stability and stress | Understanding of fundamental principles of ship construction and the theories and factors affecting trim and stability and measures necessary to preserve trim and stability Knowledge of the effect on trim and stability of a ship in the event of damage to and consequent flooding of a compartment and countermeasures to be taken Knowledge of IMO recommendations concerning ship stability | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved training ship experience .3 approved simulator training, where appropriate | Stability and stress conditions are maintained within safe limits at all times |
| Monitor and control compliance with legislative requirements and measures to ensure safety of life at sea and the protection of the marine environment | Knowledge of international maritime law embodied in international agreements and conventions Regard shall be paid especially to the following subjects: .1 certificates and other documents required to be carried on board ships by international conventions, how they may be obtained and their period of validity .2 responsibilities under the relevant requirements of the International Convention on Load Lines .3 responsibilities under the relevant requirements of the International Convention for the Safety of Life at Sea .4 responsibilities under the International Convention for the Prevention of Pollution from Ships .5 maritime declarations of health and the requirements of the International Health Regulations .6 responsibilities under international instruments affecting the safety of the ship, passengers, crew and cargo .7 methods and aids to prevent pollution of the marine environment by ships .8 national legislation for implementing international agreements and conventions | Examination and assessment of evidence obtained from one or more of the following: .1 approved in-service experience .2 approved training ship experience .3 approved simulator training, where appropriate | Procedures for monitoring operations and maintenance comply with legislative requirements Potential non-compliance is promptly and fully identified Planned renewal and extension of certificates ensures continued validity of surveyed items and equipment |
| Maintain safety and security of the ship's crew and passengers and the operational condition of life-saving, fire-fighting and other safety systems | A thorough knowledge of life-saving appliance regulations (International Convention for the Safety of Life at Sea) Organization of fire and abandon ship drills Maintenance of operational condition of life-saving, fire-fighting and other safety systems Actions to be taken to protect and safeguard all persons on board in emergencies Actions to limit damage and salve the ship following a fire, explosion, collision or grounding | Examination and assessment of evidence obtained from practical instruction and approved in-service training and experience | Procedures for monitoring fire-detection and safety systems ensure that all alarms are detected promptly and acted upon in accordance with established emergency procedures |
| Develop emergency and damage control plans and handle emergency situations | Preparation of contingency plans for response to emergencies Ship construction, including damage control Methods and aids for fire prevention, detection and extinction Functions and use of life-saving appliances | Examination and assessment of evidence obtained from approved in-service training and experience | Emergency procedures are in accordance with the established plans for emergency situations |
| Organize and manage the crew | A knowledge of personnel management, organization and training on board ship A knowledge of related international maritime conventions and recommendations, and national legislation | Examination and assessment of evidence obtained from approved in-service training and experience | The crew are allocated duties and informed of expected standards of work and behaviour in a manner appropriate to the individuals concerned Training objectives and activities are based on an assessment of current competence and capabilities and operational requirements |
| Organize and manage the provision of medical care on board | A thorough knowledge of the use and contents of the following publications: .1 International Medical Guide for Ships or equivalent national publications .2 Medical section of the International Code of Signals .3 Medical First Aid Guide for Use in Accidents Involving Dangerous Goods | Examination and assessment of evidence obtained from approved training | Action taken and procedures followed correctly apply and make full use of advice available |